HLR_GUI_1	Interactive interface	User should be able to interact with application to manipulate the rover (switch between manual and auto state)
HLR_GUI_2	Display of information	User should be able to obtain necessary information about vehicle’s condition
HLR_GUI_3	Device select	User should be able to pick COM port of radio and joystick
HLR_COMM_1	Packet management	This process should be able to interpret received packet and (if necessary) update GUI or send a response
HLR_COMM_2	Drive management	Process should receive joystick readings and send a packet to drive the motors or GPS coords in case of auto mode.
HLR_COMM_3	Connection alive	Process should set a packet and wait for response to check if connection is alive
HLR_COMM_4	Connection	Process should establish connection with devices before going further
HLR_GENERAL_1	Communication between processes	Communication between processes should be available

Req_met	LLR_GUI_1	Interactive interface	- radio buttons to choose over manual or auto mode / - stop button making the rover stop immediately and back to base / - text area to enter GPS coords / - submit coords button
Req met	LLR_GUI_2	Display of information	- visual mark that connection between rover and operating station is established / - display of GPS coords and orientation variables / - display of UNIRover system states
Req met	LLR_GUI_3	Device select	There should be a popping up window which displays available devices, enables user to refresh the list of available devices and keep the information of selected devices. In case of a wrong choice, the program should exit.
req_met	LLR_COMM_1	Packet management	Process should be interpreting packets received through a radio. Available packets: / - connection alive, / - UNIRover system states, / - sensor data handling
	LLR_COMM_2	Drive management	Comm process should be able to send packets with drive information or desired GPS coords
	LLR_COMM_3	Connection alive	Process should send repeatedly connection alive packet every 5 seconds. If response comes back later than 2 seconds, connection is considered broken
	LLR_COMM_4	Connection	Process shall establish a connection with: / - radio, / - joystick / before going further
	LLR_GENERAL_1	Communication between processes	There should be a pipe between processes. A path, which is used to share information. It should be pooled for less than 10ms.